## Slide 1
Lecture Notes: RGB and HSV Color Spaces

## Slide 2: Color Images
Are constructed from three overlaid intensity maps.
Each map represents the intensity of a different “primary” color.
The actual hues of the primaries do not matter as long as they are distinct.
The primaries are 3 vectors (or axes) that form a “basis” of the color space.

## Slide 3: Vector-Valued Pixels
Each color corresponds to a point in a 3D vector space

## Slide 4: RGB Color Space
for standard digital images
primary image colors red, green, and blue
  correspond to R,G, and B axes in color space.
8-bits of intensity resolution per color
  correspond to integers 0 through 255 on axes.
no negative values
  color “space” is a cube in the first octant of 3-space.
color space is discrete
  2563 possible colors = 16,777,216 elements in cube.

## Slide 5: Color Cube: Faces (White-Point View)
The CMY color space is …

## Slide 6: Color Cube: Faces (Black-Point View)

## Slide 7: Color Cube: Faces (inner and outer)

## Slide 8: Color Cube: Faces (inner and outer)

## Slide 9: Color Cube: Faces (inner and outer)

## Slide 10: Color Cube: Faces (inner and outer)

## Slide 11: Color Cube: Faces (inner and outer)

## Slide 12: Color Cube: Faces (inner and outer)

## Slide 13: Color Cube: Faces (inner and outer)

## Slide 14: Different Axis Sets in Color Space
RGB axes
CMY axes

## Slide 15: Color With Respect To Different Axes
The same color has different RGB and CMY coordinates.

## Slide 16: Color Images
R
G
B
L
a*
b*
are represented by three bands (not uniquely) e.g., R, G, & B or L, a*, & b*.
Red
Green
Blue
Luminance
a*-chroma
b*-chroma

## Slide 17: RGB to LHS: A Perceptual Transformation
luminance
hue
saturation
photo receptors
brain
The eye has 3 types of photoreceptors:
sensitive to red, green, or blue light.
The brain transforms RGB into separate brightness and color channels (e.g., LHS).

## Slide 18: Color Representations: Color Spaces
RGB is the most familiar color representation because our digital imaging devices use them to encode and to display images. Because they have sensors that are sensitive to red, green, and blue light, cameras transduce an image projected onto its sensor array into a matrix of 3-vectors.
The vectors may be transformed into other representations for processing or analysis. Here we consider one such representation, the HSV colorspace. It is a cylindrical coordinate representation of colors that separates the brightness (value) from the chrominance (hue and saturation).

## Slide 19: Equivalue Color Triangle
A plane through the colors
forms a triangle inside the color cube if c ≤ 255 or c ≥ 510, or a hexagon if 255 < c < 510. Every color on the planar surface is such that r + g + b = c. Therefore its value is c/3. It is on this equivalue plane that hue and saturation are computed.
c=255, v=85
HSV is defined with respect to planes that cut the cube perpendicularly to the gray line – c[1 1 1]T where c  {0,…255}. These are called equivalue planes.

## Slide 20: Equivalue Color Triangle
On the g = 0 face of the cube the triangle traces the line, r + b = 255.
c=255, v=85

## Slide 21: Color Cube: Equivalue Triangle
Notice the dark outline of the triangle. It is not there – not a real feature of the color surface. The planar discontinuities in 3D at the edges of the triangle project to abrupt changes in the color gradient in the 2D image. The change in gradient is a second order effect that is exaggerated by the color-agonist, center-surround edge detectors on the retina. It is an optical illusion.

## Slide 22: Color Cube: Equivalue Triangle
As the cube is faded out over this and the next 2 slides, the discontinuity diminishes and dark outline disappears.

## Slide 23: Color Cube: Equivalue Triangle

## Slide 24: Color Cube: Equivalue Triangle
Every point on the equivalue plane has the same value. (“well, duh!”) There is one plane for each value (r+g+b)/3. The hue and saturation for all colors with the same value are calculated in the plane.

## Slide 25: Equivalue Color Hexagon
A plane through the colors
forms a triangle inside the color cube if c ≤ 255 or c ≥ 510, or a hexagon if 255 < c < 510. Every color on the planar surface is such that r + g + b = c. Therefore its value is c/3. It is on this equivalue plane that hue and saturation are computed.
c=384, v=128

## Slide 26: Equivalue Color Hexagon
On the g = 0 face of the cube the hexagon traces the line, r + b = 383.
c=383, v=128
Right Side
Outside looking in.

## Slide 27: Equivalue Color Hexagon
On the g = 255 face of the cube the hexagon traces the line, r + b + g = 383.
Left Side
c=383, v=128
Outside looking in.

## Slide 28: Equivalue Color Hexagon
Back
Bottom
The lines on the other four faces similarly have r + b + g = 383.
Top
Front
Outside looking in.

## Slide 29: Color Cube: Equivalue Hexagon
Notice the outline of the hexagon. It is not there – not a real feature of the color surface. The planar discontinuities in 3D at the edges of the hexagon project to abrupt changes in the color gradient in the 2D image. The change in gradient is a second order effect that is exaggerated by the color-agonist, center-surround edge detectors on the retina. It is an optical illusion.

## Slide 30: Color Cube: Equivalue Hexagon
As the cube is faded out over this and the next 2 slides, the discontinuity diminishes and the virtual outline disappears.

## Slide 31: Color Cube: Equivalue Hexagon

## Slide 32: Color Cube: Equivalue Hexagon
Every point on the equivalue plane has the same value. (“well, duh!”) There is one plane for each value (r+g+b)/3. The hue and saturation for all colors with the same value are calculated in the plane.

## Slide 33: Color Cube: Equivalue Hexagon

## Slide 34: Color Cube: Equivalue Hexagon
Here the hexagon is cut out of the cube to provide another view.

## Slide 35: RGB Components of the Color Hexagon at Value 128
Red
Green
Blue
r+g+b = 384
r{0,…,255}
b{0,…,255}
g{0,…,255}

## Slide 36: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.
Equivalue plane at v = 0: single point, pure black.

## Slide 37: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 38: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 39: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 40: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 41: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 42: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 43: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 44: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.
Equivalue plane at v = 85: largest upright triangle, start of hexagonal intersections.

## Slide 45: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 46: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 47: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 48: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.
Equivalue plane at v = 128: symmetric hexagon, intersecting plane with largest area.

## Slide 49: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 50: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 51: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 52: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.
Equivalue plane at v = 170: largest inverted triangle, end of hexagonal intersections.

## Slide 53: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 54: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 55: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 56: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 57: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 58: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 59: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.

## Slide 60: Equivalue Plane Intersecting Color Cube
Projection: the gray line is perpendicular to this page.
Equivalue plane at v = 255: single point, pure white.

## Slide 61: HSV Color Representation
Color vector p0
+ marks the spot where R=G=B= (r0+g0+b0)/3
p0 = (r0, g0, b0)
intersects R, G, & B axes at r0+g0+b0, and contains p0.
lies in plane R+G+B=(r0+g0+b0),
Triangle:

## Slide 62: A Color Point on its Equivalue Plane*
*where all the colors have components r, g, & b such that r+g+b = the same constant c.

## Slide 63: The Color Vector Associated with the Color Point

## Slide 64: The Vector’s Coordinates and RGB Component Vectors

## Slide 65: The Color Cube, the Equivalue Plane, & the Gray Line*
*The point at which the gray line intersects equivalue plane is called the “gray point” .

## Slide 66: The Color Point and the Gray Line*
*“+” marks the gray point on the equivalue plane.

## Slide 67: The Saturation Component* of the Color Vector
*is a vector in the equivalue plane from the gray point to the color point; its length is the scalar saturation.

## Slide 68: The Saturation and Value Components of the Color Vector

## Slide 69: The Hue*, Saturation, and Value of the Color
*is the angle in the plane from the red line (in the plane from the gray point to the red axis) to the color point.

## Slide 70: The Hue and the Saturation on the Equivalue Plane

## Slide 71: The Hue, Saturation, and Value with the Gray Line

## Slide 72: HSV Components of the Color Hexagon at Value 128
hue
saturation
value
r+g+b = 384
s[0,1]
v = 128
h(/128){0,…,255}
s(1/255){0,…,255}

## Slide 73: HSV Components of the Color Hexagon at Value 128
hue
saturation
value
r+g+b = 384
h[0,2)
s[0,1]
v = 128

## Slide 74: HSV Color Representation
Color vector p0
+ marks the spot where R=G=B= (r0+g0+b0)/3
intersects R, G, & B axes at r0+g0+b0, and contains p0.
lies in plane R+G+B=(r0+g0+b0),
Triangle:
p0 = (r0, g0, b0)

## Slide 75: RGB to HSV Conversion
p0
v0
s0
x
v0 is the value vector.
v0 is the value – a scalar.
96

## Slide 76: RGB to HSV Conversion
96
p0
v0
s0
c/3 is the usual value-image intensity (the average of r, g, & b), …
… c √3/3 is the length of the value vector,…
x
… so there is ambiguity in the definition of v0. Its interpretation is contextual.

## Slide 77: RGB to HSV Conversion
p0
v0
s0
x
is the red line, x, for all colors with value, v0.
is the saturation vector, s0, for color p0.
is the hue angle, h 0, for color p0.
88

## Slide 78: RGB to HSV Conversion: The Red Line
Note that:
for c > 85, the red line (vector) x extends beyond the color cube, and
vector x = 0 if and only if c = 0.

## Slide 79: RGB to HSV Conversion
p0
v0
s0
x
In summary,
where c = r0 + g0 + b0 , the sum of the components of p0.
and
The dot product of (i) the unit vector in the saturation direction and (ii) the unit vector in the direction of the red line is the cosine of the hue.
The scalar saturation, s0, is the length of the saturation vector, s0.
The value is the average of the r, g, & b intensities of the color.

## Slide 80: Normalizing the Saturation
p0
v0
s0
x
which has length
The scalar saturation,
usually is normalized to lie between 0 and 1. There are a number of possible ways to do this. One is to use the largest possible length of a saturation vector in the color cube. That vector lies in the triangle with vertices [r g b]T = [255 0 0] T, [0 255 0] T, and [0 0 255] T. There are 3 such vectors, from the gray point to pure red, pure green, or pure blue. The red one is
Therefore, s0 can be replaced by .
See other approaches to normalizing the saturation on slides nnn

## Slide 81: Other Steps to Include in RGBHSV
There are a few places in the algorithm where computation can be problematic. These include division by zero, exceeding limits due to round-off errors, and values returned by library functions that are inconsistent with the RGBHSV algorithm.
Recall that the hue calculation for color, p, requires division by the product of the length of the red vector, x(p), and the length of the saturation vector, s(p). If either of these is 0, then the argument could be undefined. Matlab returns NaN for acos(0/0).
s is the zero vector whenever p is a gray level (all its components are equal). Vector x = 0 if and only if color p = 0. The workaround is to add 1 to the denominator at every pixel where either p = 0 or s = 0. Then set h = 0 at those same pixel locations. If h is complex, replace it with real(h).
If, due to finite word-length effects, the dot product evaluates to a number with magnitude ever-so-slightly greater than one, the inverse cosine will return a complex value.

## Slide 82: Other Steps to Include in RGBHSV
Inverse cosine routines, like Matlab’s acos, return angles in the range [0,], whereas the RGBHSV algorithm needs them to be in the range [0,2).
Note that [0,] if and only if b  g in p and (-,0) if and only if b > g. Therefore the workaround is to let:
where

## Slide 83: RGB to HSV Algorithm 1
Compute scalar value image, v, from RGB image, I=[r g b].
Compute vector value image, V = [v v v].
Compute vector saturation image, S = I - V.
Compute scalar saturation image, s = || S ||.
Compute red axis vector image, X = [2v –v –v].
Compute red axis scalar image, x = || X ||.
Create logical image, z(r,c) = (s(r,c)==0)|(x(r,c)==0).
Compute hue cosine image, c = (SX)/((sx)+z).
Compute hue angle image, h = cos-1(c).
Create logical image, m(r,c) = b(r,c) > g(r,c).
Adjust h = ~mh + m(2pi-h).
Normalize the saturation s = s / 208.2066.
Return [h s v]T.
A vector-geometric algorithm
110
This algorithm is written in pseudocode, not Matlab.

## Slide 84: RGB to HSV Algorithm 1
Compute scalar value image, v, from RGB image, I=[r g b].
Compute vector value image, V = [v v v].
Compute vector saturation image, S = I - V.
Compute scalar saturation image, s = || S ||.
Compute red axis vector image, X = [2v –v –v]T.
Compute red axis scalar image, x = || X ||.
Create logical image, z(r,c) = (s(r,c)==0)|(x(r,c)==0).
Compute hue cosine image, c = (SX)/((sx)+z).
Compute hue angle image, h = cos-1(c).
Create logical image, m(r,c) = b(r,c) > g(r,c).
Adjust h = ~mh + m(2pi-h).
Normalize the saturation s = s / 208.2066.
Return [h s v]T.
A vector-geometric algorithm
z and m are binary images z(r,c)==1 iff s(r,c)==0; m(r,c)==1 iff b(r,c) > g(r,c).
||  || is the norm operator – the square root of the pixel-wise sum of the squares of the image’s 3-vector components.
SX is the pixel-wise dot product of images S & X. sx is the p.w. scalar product of the scalar images s and x.
matlab: || S || = sqrt(sum(S.^2,3));
V =3-band val img

## Slide 85: A Faster Hue Calculation
Project color p0 onto the red line, x, using the dot product,
The ratio of the second dot product to the first is the tangent of the hue angle. Therefore,
Vector is perpendicular to x. Project p0 on to z to get

## Slide 86: RGB to HSV Algorithm 2
110
Compute scalar value image, v, from RGB image, I=[r g b]T.
Compute vector value image, V = [v v v]T.
Compute vector saturation image, S = I - V.
Compute scalar saturation image, s = || S ||.
Compute the scalar image, x = 2r–g–b.
Compute the scalar image, y = sqrt(3)(g-b).
Compute hue angle image, h = atan2(y,x).
Create a logical image, m(r,c) = b(r,c) > g(r,c).
Adjust h = ~mh + m(2pi+h).
Normalize s = s / 208.2066.
Return [h s v]T.
A vector-geometric algorithm
Using the expressions on the previous slide reduces the number of variables and the number of computations necessary to compute the hue. Experiments with Matlab show Algorithm 2 to be 2.7 times faster than Algorithm 1. Both algorithms return the same values.
atan2 returns angles in (-,). Negative angles are in the b>g region. They are shifted by adding them to 2.
This algorithm is written in pseudocode, not Matlab.

## Slide 87: Example RGB Image and HSV Bands
Original image
Karen Gillis Taylor, “A Fruit Color Study.”
Hue image displayed with a primary color color-map
Saturation image scaled to (0,…,255)
Value Image

## Slide 88: HSV to RGB Conversion
ˆ
ˆ
ˆ
form an orthonormal basis with respect to the equivalue plane.
The equivalue plane is perpendicular to the value vector, v.
The plane contains vector x defined on slide 77.
Therefore, v is perpendicular to x and y = v  x is also in the plane.
If we keep the directions but ignore the magnitudes, the unit vectors
This conversion requires a change of coordinates through a rotation and a translation.

## Slide 89: HSV to RGB Conversion
ˆ
ˆ
ˆ
Given values h, s, and v, where
the saturation vector is
with respect to unit vectors x, y, and v, in the equivalue plane.
ˆ
ˆ
ˆ
Since the x- and y-axes lie in the equivalue plane and the cdt. origin is the gray point, we set v = 0 for now.

## Slide 90: HSV to RGB Conversion
ˆ
ˆ
ˆ
Given values h, s, and v, where
the saturation vector is
with respect to unit vectors x, y, and v, in the equivalue plane.
ˆ
These are the coordinates of s with respect to x, y, & v.
ˆ
ˆ
ˆ
This is s written as a linear combination of vectors x, y, & v.
ˆ
ˆ
ˆ
If s is in the range 0 to 1, then it must be denormalized first by multiplying by smax.

## Slide 91: HSV to RGB Conversion
ˆ
ˆ
ˆ
ˆ
ˆ
ˆ
We need to find r0, g0, & b0…
x, y, and v, are not in the same directions as the red, green, and blue unit vectors, r, g, and b.
Therefore, [s]xyv , which we know, is not equal to [s]rgb , which we do not know, but need in order to find the color, p0, with respect to r, g, and b.

## Slide 92: HSV to RGB Conversion
ˆ
ˆ
ˆ
ˆ
ˆ
ˆ
The specific numbers in [s]rgb and in [s]xyv (that represent the point w.r.t. the two coordinate systems) are, however, different.
but
and
Vector s written as a linear combination of vectors, r, g, and b, and s written as a linear combination of vectors, x, y, and v both refer to the same point on the equivalue plane.
… which means we need to find the x, y, & v unit vectors in terms of the r, g, & b unit vectors.

## Slide 93: HSV to RGB Conversion
ˆ
ˆ
ˆ
ˆ
ˆ
ˆ
Then,
We can find r0, g0, and b0, from h0, s0, and v0, if we know how the unit vectors x, y, and v, are expressed with respect to r, g, and b. That relationship is in the form of a rotation matrix, A, such that,
96

## Slide 94: HSV to RGB Conversion
ˆ
ˆ
ˆ
ˆ
ˆ
ˆ
When written w.r.t the xyz coordinate system we have
So that,
But that implies,
The columns of the rotation matrix, A, are the x, y, & v unit vectors in rgb coordinates.

## Slide 95: HSV to RGB Conversion
ˆ
ˆ
ˆ
ˆ
ˆ
ˆ
v is the unit vector in the direction [1 1 1]T when written w.r.t rgb coordinates.
ˆ
x is perpendicular to v and has equal g and b components.
ˆ
ˆ
ˆ
ˆ
y is the cross product of v with x.
ˆ
ˆ
ˆ
How to find the x, y, & z unit vectors in rgb coordinates:

## Slide 96: HSV to RGB Conversion
p0
v0
s0
Therefore, the rotation matrix is
Substitute that into the 2nd equation on slide 93 to get:
Finally, [s]rgb must be translated to the value vector to obtain the rgb color of p0:
where s0 = [s]rgb and [v]rgb= v0 as def ’d. on slide 75.
The x, y, & z unit vectors in rgb coordinates are the columns of the rotation matrix:

## Slide 97: HSV to RGB Algorithm
Reshape RC images h, s, and v into RC1 column vectors.
Denormalize the saturation image, s = 208.2066s.
Compute the x-coordinate image, x = scos(h).
Compute the y-coordinate image, y = ssin(h).
Construct the value vector image, V = [v v v]T
Construct the 1st two columns of rotation matrix A
Rotate the saturation image S = [s1 s2 s3]T = A[x y]T.
Add the result to V to recover IRGB = S + V.
Round IRGB, convert it to uint8, and reshape it to RC3.
A vector-geometric algorithm
This inverts the outputs of both Algorithm 1 and Algorithm 2.
Note: V is 3xRC, since v is an RCx1 column vector and V = [v v v]T.
A3x2 multiplies [x y]T which is 2xRC.
Lines 7 & 8: S, V, and IRGB are 3xRC.
Note: if size(X) == [R C B], then size(X(:)) == [RCB 1].

## Slide 98: Alternative HSV Representations
The HSV algorithms presented in the first part of this lecture are direct implementations of the vector math.
One of the problems with the direct approach is that it is that the presence of transcendental functions increases the time necessary to convert an image.
To use HSV at video frame rate requires a simpler algorithm that yields a reasonable approximation to the direct implementation.
v=(r+g+b)/3.
V = [v v v]T.
S = I - V.
s = || S ||.
X = [2v –v –v]T.
x = || X ||.
z(r,c) = … (s(r,c)==0)|(x(r,c)==0).
c = (SX)/((sx)+z).
h = cos-1(c).
m(r,c) = b(r,c) > g(r,c).
h = ~mh + m(2pi-h).
s = s / 208.2066.
Return [h s v]T.

## Slide 99: Hexagonal Projection Representations
Faster algorithms use a hexagonal projection of the color cube. To generate the hexagon, rotate the color cube in 3-space then project it along its gray line (the diagonal from white to black) onto a chromaticity plane. The result is a hexagon that has the 6 primary colors – red, yellow, green, cyan, blue, and magenta – at its vertices.
rgb color vector, p, is projected on the hexagon where its hue and saturation are computed.

## Slide 100: Hexagonal Projection Representations
Faster algorithms use a hexagonal projection of the color cube. To generate the hexagon, rotate the color cube in 3-space then project it along its gray line (the diagonal from white to black) onto a chromaticity plane. The result is a hexagon that has the 6 primary colors – red, yellow, green, cyan, blue, and magenta – at its vertices.
rgb color vector, p, is projected on the hexagon where its hue and saturation are computed.

## Slide 101: A Fast RGB to HSV Algorithm
Given color p0 = [R G B]T where R, G, B {0,…,255}, to compute [h s v]T where s, v [0,1] and h [0,360) the algorithm proceeds as follows:
Reference: HSL and HSV - Wikipedia, the free encyclopedia
Compute [r g b] = [R G B]/255.
Set m = min(r,g,b) , M = max(r,g,b).
Set v = M.
Compute C = M – m.
If C == 0 then s=0, h=0. Return [h s v]T.
s = C/M.
If M==r then h = ((g-b)/c) modulo 6.
else if M==g then h = 2 + (b-r)/c.
else h = 4 + (r-g)/c.
h = 60h.
This algorithm is based on the hex projection.
Experiments with Matlab show this algorithm to be 3 times faster than Algorithm 1 and 1.13 faster than Algorithm 2. The numbers output by this one differ from the other two.
111
R,G,B are numbers here not images.

## Slide 102: A Fast HSV to RGB Algorithm
Given vector h0T = [h s v] where h  [0, 360), s  [0, 1], and v  [0, 1], to compute p0T = [r g b] where r, g, b  {0, …, 255}:
Reference: HSL and HSV - Wikipedia, the free encyclopedia
H = h/60.
C = vs.
D = v-C.
X = C(1 - |(H mod 2)-1|).
if 0  H < 1 then [r g b] = [C X 0]
else if 1  H < 2 then [r g b] = [X C 0]
else if 2  H < 3 then [r g b] = [0 C X]
else if 3  H < 4 then [r g b] = [0 X C]
else if 4  H < 5 then [r g b] = [X 0 C]
else if 5  H < 6 then [r g b] = [C 0 X]
else [r g b] = [0 0 0]
[r g b] = 255*[r+D g+D b+D]
This algorithm is the inverse of the previous one.
109
h, s, & v are numbers here not images.

## Slide 103: Comparison of the Two Algorithms
p0
v0
s0
x
Geometric representation on the equivalue plane
Projection of the color on the choma-hexagon.

## Slide 104: Geometric Hexagonal Projection
Reference: HSL and HSV - Wikipedia, the free encyclopedia
Given a color, its value is the projection, parallel to the hexagon, of the rgb point onto the gray line scaled by .
Its hue is the angular distance around the hexagon from the projection of the red axis to the color, projected parallel to the gray line.
The saturation is the ratio of the distance from the gray line to the projected color, [0,p0], to the distance from the gray line to one of the vertices of the hexagon.
To compute the projection of a color we must find the rotation matrix for the cube.

## Slide 105
Rotation of the Color Cube
Rotations for projection onto the hexagon:
Original cube viewed along the green axis.
Rotated 45 around the green axis.
Rotated cube viewed along the red axis.
Rotated 35.26 around the red axis.
Final pose viewed along the green axis.
(a)
(b)
(c)
(d)
(e)

## Slide 106: Rotation of the Color Cube
Rotated cube corners:
Cube corners:
Rotation matrix:
Projected, rotated cube corners:
Here’s the math.
110

## Slide 107: Rotation of the Color Cube
Rotated cube corners:
Cube corners:
Rotation matrix:
Projected, rotated cube corners:
Here’s the math.
45 around green
35.26 around red
Now the 3rd dimension is along the gray line.
Projection: set 3rd dim to 0.
6 primaries + black and white

## Slide 108: Rotation and Projection of the Color Cube
Chromaticity-plane hexagon with red, yellow, green, cyan, blue, and magenta vertices.
The origin of this rectangular coordinate system is at the gray point in the center of the hexagon. The y-axis is vertical through the green point; the x-axis is to the right through orange.
y
x

## Slide 109: Rotation and Projection of the Color Cube
Chromaticity-plane hexagon with red, yellow, green, cyan, blue, and magenta vertices.
The origin of this rectangular coordinate system is at the gray point in the center of the hexagon. The y-axis is vertical through the green point; the x-axis is to the right through orange.
… but the red and blue axes project 60 on either side of green.
The green axis of the hexagon remains aligned with the green axis of the original color cube, …
y
x

## Slide 110: Geometric Hexagonal Projection
color projection onto the hexagon
Use color p0 = [128 50 206]T as an example. Rotating p0 with the matrix on slide 106 yields
The red axis is -30 from the hexagon’s x-axis and p0’s blue component is larger than its green. Therefore,
So we get (h,s,v) = (270, 0.5298, 128) which is exactly what we got from the geometric algorithms (slides 83 & 86).

## Slide 111: Fast Algorithm for RGB to HSV
The fast algorithm on slide 100 uses the hex projection without rotating the color. First the RGB values are normalized by dividing them by the maximum intensity. The test color then scales to
color projection onto the hexagon
The value of the color is taken to be simply the maximum of the normalized rgb values. Therefore v0 = 0.8078, whereas the geometric algorithm, if normalized would have yielded v0 = 0.5.

## Slide 112: Fast Algorithm for RGB to HSV
To project the color onto the hexagon the fast algorithm subtracts the minimum of the rgb intensities from all three. The reasoning is:
Let p0 = p0  mv for v, the unit vector in the direction of the gray line and m a real number. The value of m shifts p0 up or down in the direction of the gray line. The result projects to the same point, p0proj, in the hexagon independent of the value of m.
If m is min(r,g,b), then the color is shifted to one of the faces of the original color cube.
v = [1 1 1]T
color projection onto the hexagon

## Slide 113: Fast Algorithm for RGB to HSV
Subtract m from p0 to get
which is in the BR-plane of the color cube, since G = 0. (See slide 100.) Note that p0 projects to the same point on the hexagon as does p0.
For our test color,
color projection onto the hexagon

## Slide 114: Fast Algorithm for RGB to HSV
Hue is defined with respect to chroma as
Define the chroma as C = M – m. This definition is justified by noting that
Chroma C = 0 for any color on the gray line
any color with two zero components is a primary,
for any color with one zero component the formula makes C equal the maximum of the two nonzero values.
color projection onto the hexagon

## Slide 115: Fast Algorithm for RGB to HSV
So, for
We get
color projection onto the hexagon
which is exactly the hue from the geometric algorithms.

## Slide 116: Fast Algorithm for RGB to HSV
Saturation is defined with respect to chroma and value as
Value is defined as either
color projection onto the hexagon

## Slide 117: Fast Algorithm for RGB to HSV
Saturation is defined with respect to chroma and value as
Therefore with the color p0 we have

## Slide 118: Hue and Saturation via Projection onto the Hexagon
For color p0 = [128 50 206]T we have three different HSV triples,
by vector math,
by the first hexagon projection,
and by the second hexagon projection,

## Slide 119: Example RGB Image and HSV Bands
Original image
Karen Gillis Taylor, “A Fruit Color Study.”
Hue image displayed with a primary color color-map
Saturation image scaled to (0,…,255)
Value Image
Fast Algorithm

## Slide 120: Example RGB Image and HSV Bands
Original image
Karen Gillis Taylor, “A Fruit Color Study.”
Hue image displayed with a primary color color-map
Saturation image scaled to (0,…,255)
Value Image
Algorithms 1 & 2

## Slide 121: Maxwell’s Triangle
D. Malacara-Hernandez, Color Vision and Colorimetry: Theory and Applications, SPIE Press, (2002).
Probably the first attempts to produce color curves describing the trichromatic theory of color were those by Maxwell (1857, 1860).… [The] first chromaticity diagram was a circle devised by Newton. Later, Maxwell used an equilateral triangle.… In his trichromatic theory, each of the three primary colors—red, green, and blue—is located at a corner of the triangle. The white color is in the middle. Other colors are formed by a combination of the r, g, b components depending on the distances from each of the three sides of the triangle. This triangular representation has been used often with several modifications.

## Slide 122: Brightness + Chrominance Representation
There are many different ways to encode color in terms of 1D brightness and 2D chrominance. Chrominance is often represented in terms of hue and saturation. A given brightness measure (e.g. value or NTSC luminance) defines a planar surface in the color cube on which the brightness is constant. One point on that surface is gray. The saturation of any color with the given brightness is defined as the distance on the plane from the color to the gray point. The hue is defined as the angular deviation from red measured in the same plane.

## Slide 123: Brightness + Chrominance Representation
The HSV encoding scheme presented in the first part of this lecture is a direct implementation of the vector math. Although it is nonstandard, it demonstrates the ideas that underlie most of these representations.
For a good explanation of more standard HSV and LHS representations please see:
HSL and HSV - Wikipedia, the free encyclopedia.
An explanation of the hexagonal representation of HSV is given later in this lecture.

## Slide 124: C.I.E. 1931 Color Space
1http://hyperphysics.phy-astr.gsu.edu/hbase/vision/cie.html
“The CIE system characterizes colors by a luminance parameter Y and two color coordinates x and y which specify the point on the chroma-ticity diagram. This system['s] ... parameters are based on the spectral power distribution ... of the light emitted from a colored object and are factored by sensitivity curves which have been measured for the human eye.”1
Commission Internationale de l’Éclairage Uniform Color Scale
This is not a simple slice through the color cube. It is a continuous mapping from the 3D cube onto a 2D plane that warps the color distribution.

## Slide 125: C.I.E. 1931
2https://en.wikipedia.org/wiki/CIE_1931_color_space
3https://en.wikipedia.org/wiki/Munsell_color_system
This 1931 chromaticity diagram shows a single xy plane in the xyY color space.
“The CIE 1931 color space chromaticity diagram rendered in terms of the colors of lower saturation and value than those displayed in the diagram above that can be produced by pigments, such as those used in printing. The color names are from the Munsell color system.”2,3
127

## Slide 126: C.I.E. 1976 U.C.S.
http://hyperphysics.phy-astr.gsu.edu/hbase/vision/cie1976.html
(L, u, v) color space
This diagram, produced by the C.I.E. in 1976 specifies the range of colors perceptible at a single luminance, L, by an average person. On the periphery the colors are monochromatic colors labeled with the corresponding wave-lengths of light. The white point is intersected by a curve that displays the corresponding black body temperature. (u, v) are the CIE chromaticity coordinates. The distance between points is related to the perceptual difference in color.

## Slide 127: C.I.E. 1976 U.C.S.
(L, u, v) color space regions
http://hyperphysics.phy-astr.gsu.edu/hbase/vision/cie1976.html
Color regions on a slightly desaturated CIE 1976 Luv color space similar to those on the CIE 1931 xyY digram on slide 125.
Point c0 on the line between colors c1 and c1 is the color that would be obtained by mixing the two endpoint colors in proportion to the distances from the endpoints. E.g.
where 0  1.

## Slide 128: Color Gamuts
A color gamut is the range of colors that can be represented by a given display. The pure R, G, and B values are plotted on a CIE chromaticity diagram. The colors inside the triangle are the ones that can be displayed by the device.

## Slide 129: Color Gamuts
Since the display you are looking at is probably sRGB …
…the colors you see in the CIE diagram are actually …
…inside this triangle …
…and all the colors outside the triangle cannot be displayed …
… even though you could see them on a better display (like reality!)




