## Slide 1
Lecture Notes: The 1&2-Dimensional Fourier Transforms
This work is licensed under the Creative Commons Attribution-Noncommercial 2.5 License. To view a copy of this license, visit http://creativecommons.org/licenses/by-nc/2.5/ or send a letter to Creative Commons, 543 Howard Street, 5th Floor, San Francisco, California, 94105, USA.

## Slide 2: Signal:
A measurable phenomenon that changes over time, throughout space, or both.
01101000101101110110010110001
sound
image
code

## Slide 3: Signals: Space/Time vs. Frequency-Domain Representation
Space/time representation: a graph of the measurements with respect to a point in time and/or positions in space.
Fact: signals undulate (otherwise they’d contain no information).
Frequency-domain representation: an exact description of a signal in terms of its undulations.

## Slide 4: Example: Time-Domain Representation

## Slide 5: Example: Frequency-Domain Representation

## Slide 6: Origin of Sounds
The mechanical vibrations of an object in an atmosphere.
Vibrations: internal elastic motions of the material.
The surface of the object undulates causing compressions and rarefactions in the air which propagate through the air away from the surface.
An object vibrates with different modes.
A mode is a vibratory pattern with a distinctive shape — part of the object surface moves out while another part moves in — a standing wave.

## Slide 7: Vibratory Modes / Standing Waves: Examples
displacement from rest position
string modes
internal pressure
pipe modes
Note that the negatives of these also will occur
Note that the modes are all sinusoids.

## Slide 8: Sound Waves:
string sound
pipe sound
Emerge from the superposition of the modes.

## Slide 9: Sound Waves:
string sound
pipe sound
Emerge from the superposition of the modes.
The vibratory modes add up to one complex motion that pushes the air around the vibrating object
Even-order harmonics
Odd-order harmonics

## Slide 10: Fact: Any Real Signal has a Frequency-Domain Representation
The modes shown (blue) sum to the rippling square wave (black).
As the number of modes in the sum becomes large, it approaches a square wave (red).
Odd-order harmonics

## Slide 11: Frequency-Domain Representation
The sinusoids are called “basis functions”.
Any periodic signal can be described by a sum of sinusoids.
The multipliers are called “Fourier coefficients”.

## Slide 12: Frequency-Domain Representation
The sinusoids are called “basis functions”.
Any periodic signal can be described by a sum of sinusoids.
The multipliers are called “Fourier coefficients”.
Basis functions

## Slide 13: Frequency-Domain Representation
The sinusoids are called “basis functions”.
The multipliers are called “Fourier coefficients”.
Any periodic signal can be described by a sum of sinusoids.
The Fourier coefficients(of a square wave).

## Slide 14: Example: Partial Sums of a Square Wave
1 sine
2 sines
4 sines
8 sines
16 sines
32 sines
The limit of the given sequence of partial sums1 is exactly a square wave
1 the limit as n becomes large of the sum of n sines.

## Slide 15: Anatomy of a Sinusoid
f (t)
0

## Slide 16: The Inner Product: a Measure of Similarity

## Slide 17
Inner Products
a function, f
g is a component of f
pointwise product: f(t)g(t)
sum of the area 0

## Slide 18
Inner Products
h is a not a comp. of f
pointwise product: f(t)h(t)
a function, f
sum of the area = 0

## Slide 19: Inner Product of a Periodic Function and a Sinusoid
3 different representations

## Slide 20: Inner Product of a Periodic Function and a Sinusoid
real number results yield the amplitude of that sinusoid in the function.

## Slide 21: Inner Product of a Periodic Function and a Sinusoid
Complex number result yields the amplitude and phase of that sinusoid in the function.

## Slide 22: The Fourier Series
is the decomposition of a -periodic signal into a sum of sinusoids.
Fourier coefficients are generated by taking the inner product of the function with the basis.
The representation of a function by its Fourier Series is the sum of sinu-soidal “basis functions” multiplied by coefficients.
The basis functions correspond to modes of vibration.

## Slide 23: The Fourier Series
can also be written in terms of complex exponentials

## Slide 24: The Fourier Series
Relationship between the real and the complex Fourier Series
Cont’d. on next page.
The sine-plus-cosine form results from the projection of f onto a cosine that is in phase with the current time.

## Slide 25: Relationship between the real and the complex Fourier Series (cont’d.)
Then add zero to the equation at the end of the previous page:
Cont’d. on next page.
Claim:
Therefore:
Thus:
Proof given at end of lecture

## Slide 26: Relationship between the real and the complex Fourier Series (cont’d.)
Then some algebraic manipulations lead to the result.

## Slide 27: Relationship between the real and the complex Fourier Series (cont’d.)
Then some algebraic manipulations lead to the result.

## Slide 28: Why are Fourier Coefficients Complex Numbers?
intensity
frequency, ω = 1/λ
0
Cn represents the amplitude, A=|Cn|, and relative phase, f , of that part of the original signal, f (t), that is a sinusoid of frequency wn = 2n / l.
0

## Slide 29: What about real + imaginary?
The FS of a cosine is a pair of impulses with complex amplitudes

## Slide 30: Real + Imaginary to Magnitude & Phase
The real and imaginary parts at the positive frequency, N/l ...
… form a magnitude, NA/2, and a phase, f0.



## Slide 31: Real + Imaginary to Magnitude & Phase
The real and imaginary parts at the negative frequency, -N/l ...
… form a magnitude, NA/2, and a phase, -f0.



## Slide 32: Fourier Series of a Square Wave
Time-domain signal
Fourier magnitude
Fourier phase

## Slide 33: The Fourier Transform
is the decomposition of a nonperiodic signal into a continuous sum* of sinusoids.
* i.e., an integral.

## Slide 34: Mammals Use the FT in Hearing

## Slide 35: The Discrete Fourier Transform

## Slide 36: The Two-Dimensional Fourier Transform
Explains why down-sampling can add distortion to an image and shows how to avoid it.
Useful for certain types of noise reduction, deblurring, and other types of image restoration.
For feature detection and enhancement, especially edge detection.
Primary Uses of the FT in Image Processing:

## Slide 37: The Fourier Transform: Discussion
The expressions
for the Fourier coefficients are “inner products” which can be thought of as measures of the similarity between the functions
continuous signals defined over all real numbers
discrete signals with N terms or samples.

## Slide 38: The Fourier Transform: Discussion (cont’d.)
In the context of inner products, the complex exponentials
are called “orthogonal sets” since they have the property:
They are called “basis sets” since for any function1, f (t), of a real variable there exists a complex-valued function F(w), and for any sequence1, hk , there exist complex numbers, Hn , such that
1 with finite energy.
The function sets are called “orthogonal basis sets”

## Slide 39: The Fourier Transform: Discussion (cont’d.)
Consider the 2-dimensional functions
These are, likewise, orthogonal:

## Slide 40: The Fourier Transform: Discussion (cont’d.)
Therefore
are orthogonal basis sets. This suggests that function f (x,y) defined on the real plane, and sequence {{ hmn }} for integers m and n have analogous Fourier representations,
where the Fourier coefficients are given by
(True for finite energy functions f (x,y) and {{ hmn }}.)

## Slide 41: Continuous Fourier Transform
The continuous Fourier transform assumes a continuous image exists in a finite region of an infinite plane.
The BoingBoing Bloggers

## Slide 42: Discrete Fourier Transform
The discrete Fourier transform assumes a digital image exists on a closed surface, a torus.
The BoingBoing Bloggers

## Slide 43: Discrete Fourier Transform
The discrete Fourier transform assumes a digital image exists on a closed surface, a torus.
The BoingBoing Bloggers

## Slide 44: The 2D Fourier Transform of a Digital Image
Let I(r,c) be a single-band (intensity) digital image with R rows and C columns. Then, I(r,c) has Fourier representation
where
are the R x C Fourier coefficients.
these complex exponentials are 2D sinusoids.

## Slide 45: Matlab’s Discrete Fourier Transforms
are implemented using some variant of the Cooley-Tukey Fast Fourier Transform algorithm1. They include the 1-D fft and ifft and the 2-D fft2 and ifft2. The 1-D versions compute
1See https://en.wikipedia.org/wiki/Cooley–Tukey_FFT_algorithm
where

## Slide 46: Matlab’s Discrete Fourier Transforms
The 2-D versions compute
where
On the Matlab command line: fft2(I) = fft(fft(I).’).’;

## Slide 47: What are 2D sinusoids?
Cont’d. on next page.
where
To simplify the situation assume R = C = N. Then
Write
Then by Euler’s relation,
Note: since images are indexed by row & col with r down and c to the right, θ is positive in the clockwise direction.

## Slide 48: What are 2D sinusoids? (cont’d.)
Both the real part of this,
and the imaginary part,
are sinusoidal “gratings” of unit amplitude, period  and direction .
Then
is the radian frequency, and
the frequency, of the wavefront
and
is the wavelength in pixels in the wavefront direction.

## Slide 49: 2D Sinusoids:
orientation
are plane waves with grayscale amplitudes, periods in terms of lengths, ...
A
q
f = phase shift

## Slide 50: 2D Sinusoids:
... specific orientations,
and phase shifts.
orientation

## Slide 51: The Fourier Transform of an Image
I
Re[F{I}]
Im[F{I}]
u
v
u
v
r
c

## Slide 52: Points on the Fourier Plane
If R=C=N the point at column freq. u and row freq. v represents a sinusoid with freq. ω and orientation θ.
If R ≠ C then ω = 1/λ where λ is the length of vector (C/u, R/v) and the wavefront orientation is θ = tan-1[(v/R)/(u/C)].

## Slide 53: Points on the Fourier Plane (of a Digital Image)
-v direction
u direction
 direction
(0,0)
and the wavelength in the wavefront direction is
of a digital image
More about this later (pp. 73-94).
Note that the wave front direction = θ only if R=C.
In the Fourier transform of an RC digital image, positions u and v indicate the number of repetitions of the sinusoid in those directions. Therefore the wavelengths along the column and row axes are
The wavefront direction is given by
row freq.
──────── column freq.
The frequency is the fraction of the sinusoid traversed over one pixel,

## Slide 54: Points on the Fourier Plane
This point represents this particular sinusoidal grating
x
y
Note that θ is the wavefront direction only if R=C.

## Slide 55: The Value of a Fourier Coefficient …
… is a complex number with a real part and an imaginary part.
If you represent that number as a magnitude, A, and a phase, f, …
..these represent the amplitude and offset of the sinusoid with frequency w and direction q.*
*See p. 51.

## Slide 56: The Value of a Fourier Coefficient
The magnitude and phase representation makes more sense physically…
…since the Fourier magni-tude, A (w,q), at point (w,q) represents the amplitude of the sinusoid…
and the phase, f(w,q), represents the offset of the sinusoid relative to origin.

## Slide 57: The Fourier Coefficient at (u,v)
So, the point (u,v) on the Fourier plane…
…represents a sinusoidal grating of frequency  and orientation .*
…represents the ampli-tude, A, and the phase offset, f, of the sinusoid.
The complex value, F(u,v), of the FT at point (u,v)…
*See p. 51.

## Slide 58: The Sinusoid from the Fourier Coeff. at (u,v)
Note that the wave front direction = θ only if R=C.

## Slide 59: FT of an Image (Magnitude + Phase)
I
log{|F{I}|2+1}
Ð[F{I}]

## Slide 60: FT of an Image (Real + Imaginary)
I
Re[F{I}]
Im[F{I}]

## Slide 61: The Power Spectrum
The power spectrum of a signal is the square of the magnitude of its Fourier Transform.
For display, the log of the power spectrum is often used.
At each location (u,v) it indicates the squared intensity of the frequency component with period and orientation
For display in Matlab:
PS = fftshift(2*log(abs(fft2(I))+1));

## Slide 62: On the Computation of the Power Spectrum
The power spectrum (PS) is defined by .
We take the base-e logarithm of the PS in order to view it. Otherwise its dynamic range could be too large to see everything at once. We add 1 to it first so that the minimum value of the result is 0 rather than –infinity, which it would be if there were any zeros in the PS. Recall that
log( f 2) = 2log( f ).
Multiplying by 2 is not necessary if you are generating a PS for viewing, since you'll probably have to scale it into the range 0-255 anyway. It is much easier to see the structures in a Fourier plane if the origin is in the center. Therefore we usually perform an fftshift on the PS before it is displayed.
>> PS = fftshift(log(abs(fft2(I))+1));
>> M = max(PS(:));
>> image(uint8(255*(PS/M)));
If the PS is being calculated for later computational use -- for example the autocorrelation of a function is the inverse FT of the PS of the function -- it should be calculated by
>> PS = abs(fft2(I)).^2;

## Slide 63: The Uncertainty Relation
A small object in space has a large frequency extent and vice-versa.
FT
space
frequency
space
frequency
FT

## Slide 64: The Uncertainty Relation
Recall: a symmetric pair of impulses in the frequency domain becomes a sinusoid in the spatial domain.
A symmetric pair of lines in the frequency domain becomes a sinusoidal line in the spatial domain.
IFT
space
frequency
 small extent 
 small extent 
 large extent 
 large extent 
space
frequency
 large extent 
 small extent 
 small extent 
 large extent 
IFT

## Slide 65: The Fourier Transform of an Edge
edge
Power Spectrum
Phase Spectrum

## Slide 66: The Fourier Transform of a Bar
bar
Power Spectrum
Phase Spectrum

## Slide 67: Some Fourier Transform Pairs
Table: Richard Szeliski, Computer Vision and Applications, Springer, 2010, ISBN 978-1-84882-935-0, p.137, http://szeliski.org/Book/.

## Slide 68: Fourier Transform Pairs

## Slide 69: 2D Fourier Transform Properties
Linearity
Shifting
Modulation
Convolution
Multiplication
Separability
Parseval Thm.

## Slide 70: Coordinate Origin of the FFT
Center =
(floor(R/2)+1, floor(C/2)+1)
Even
Even
Odd
Odd
Image Origin
Weight Matrix Origin
Image Origin
Weight Matrix Origin
After FFT shift
After IFFT shift
After FFT shift
After IFFT shift

## Slide 71: Matlab’s fftshift and ifftshift
J = fftshift(I):
I (1,1)  J ( R/2 +1, C/2 +1)
I = ifftshift(J):
J ( R/2 +1, C/2 +1)  I (1,1)
where x = floor(x) = the largest integer smaller than x.
from FFT2
or ifftshift
after fftshift
origin
origin

## Slide 72: Matlab’s fftshift and ifftshift
5 | 6 |  |  | 4
8 | 9 |  |  | 7
2 | 3 |  |  | 1
 | 1 | 2 | 3 | 
 | 4 | 5 | 6 | 
 | 7 | 8 | 9 | 
J = fftshift(I):
I (1,1)  J ( R/2 +1, C/2 +1)
I = ifftshift(J):
J ( R/2 +1, C/2 +1)  I (1,1)
where x = floor(x) = the largest integer smaller than x.
 | 1 | 2 | 3 | 
 | 4 | 5 | 6 | 
 | 7 | 8 | 9 | 
5 | 6 |  |  | 4
8 | 9 |  |  | 7
2 | 3 |  |  | 1

## Slide 73: Points on the Fourier Plane (of a Digital Image)
-v direction
u direction
 direction
(0,0)
and the wavelength in the wavefront direction is
of a digital image
Note that the wave front direction = θ only if R=C.
In the Fourier transform of an RC digital image, positions u and v indicate the number of repetitions of the sinusoid in those directions. Therefore the wavelengths along the column and row axes are
The wavefront direction is given by
row freq.
──────── column freq.
The frequency is the fraction of the sinusoid traversed over one pixel,

## Slide 74: Geometrical Derivation of Wavelength
Since the wavelength of a horizontal* wave is R/v and that of a vertical is C/u, the line segment, h, that connects the two distances is parallel to the wavefront. The wavelength is the “altitude” of the triangle w.r.t. h (the perpendicular to h that intersects the origin). The area of the triangle, one half of base times height, is independent of the leg that is taken to be the base. Equate the expression with base C/u to that with base h, to find  w.r.t R, C, v, u, & h. Then replace h with its expression as a function of R, C, v, & u to get the final expression.
*The equivalue lines are horizontal in a wave with a vertical wave front and vice versa.

## Slide 75: Coordinates and Directions in the Fourier Plane
Since rows increase down and columns to the right, slopes and angles are opposite those of a right-handed coordinate system.
increasing rows
increasing cols
(+r,+c)
(+r,-c)
(-r,-c)
(-r,+c)
q < 0
q < 0
negative slope
decreasing rows
decreasing cols
(+r,+c)
(+r,-c)
(-r,-c)
(-r,+c)
q > 0
q > 0
positive slope

## Slide 76: Inverse FFTs of Impulses
highest-possible-frequency horizontal sinusoid (C is even)
“horizontal” is the wavefront direction.
fftshifted

## Slide 77: Inverse FFTs of Impulses
highest-possible-frequency vertical sinusoid (R is even)
“vertical” is the wavefront direction.
fftshifted

## Slide 78: Inverse FFTs of Impulses
highest-possible-freq horizontal+vertical sinusoid (R & C even)
a checker-board pattern.
fftshifted

## Slide 79: Inverse FFTs of Impulses
fftshifted
lowest-possible-frequency horizontal sinusoid
“horizontal” is the wavefront direction.

## Slide 80: Inverse FFTs of Impulses
fftshifted
lowest-possible-frequency vertical sinusoid
“vertical” is the wavefront direction.

## Slide 81: Inverse FFTs of Impulses
fftshifted
lowest-possible-frequency negative diagonal sinusoid
“negative diagonal” is the wavefront direction.

## Slide 82: Inverse FFTs of Impulses
fftshifted
lowest-possible-frequency positive diagonal sinusoid
“positive diagonal” is the wavefront direction.

## Slide 83
+v direction
+u direction
512 columns
384 rows
frequencies: (u,v) = (4,3); wavelengths: (u, v) = (128,128)
Note this …
… and this.
How can that be?
Frequencies and Wavelengths in the Fourier Plane

## Slide 84
frequencies: (u,v) = (1,0); wavelength: u= 512
u = # of complete cycles in the horizontal direction
λu = C / u
512 columns
384 rows
Frequencies and Wavelengths in the Fourier Plane

## Slide 85
frequencies: (u,v) = (0,1); wavelength: v= 384
v = # of complete cycles in the vertical direction
λv = R / v
512 columns
384 rows
Frequencies and Wavelengths in the Fourier Plane

## Slide 86
Frequencies and Wavelengths in the Fourier Plane
frequencies: (u,v) = (2,0); wavelength: u= 256
u = # of complete cycles in the horizontal direction
λu = C / u
512 columns
384 rows

## Slide 87
Frequencies and Wavelengths in the Fourier Plane
frequencies: (u,v) = (0,2); wavelength: v= 192
v = # of complete cycles in the vertical direction
λv = R / v
512 columns
384 rows

## Slide 88
Frequencies and Wavelengths in the Fourier Plane
u = # of complete cycles in the horizontal direction
λu = C / u
512 columns
384 rows
frequencies: (u,v) = (3,0); wavelength: u= 170

## Slide 89
Frequencies and Wavelengths in the Fourier Plane
frequencies: (u,v) = (0,3); wavelength: v= 128
v = # of complete cycles in the vertical direction
λv = R / v
512 columns
384 rows

## Slide 90
Frequencies and Wavelengths in the Fourier Plane




512 columns
384 rows
In the Fourier plane of a square image, the orientation of the line through the point pair = the orientation of the wave front in the image. Not so for a non-square image.
In the F plane the angle is -45˚ in this image it’s about -53˚ (yellow line). That’s because the fraction of R covered by one pixel is 4/3 the fraction of C covered by one pixel.
Also as a result, the wavelength is 102.4.
frequencies: (u,v) = (3,3); wavelengths: (u, v) = (170 ,128)

## Slide 91
frequencies: (u,v) = (3,3); wavelengths: (u, v) = (170 ,128)


wf
wf
lwf
Frequencies and Wavelengths in the Fourier Plane
512 columns
384 rows
and the wavelength is:
In general the slope of the wavefront direction in the image is given by (v/R) / (u/C). Therefore its angle is

## Slide 92
Frequencies and Wavelengths in the Fourier Plane
512 columns
384 rows
frequencies: (u,v) = (3,3); wavelengths: (u, v) = (170 ,128)

## Slide 93
Frequencies and Wavelengths in the Fourier Plane
frequencies: (u,v) = (4,3); wavelengths: (u, v) = (128,128)
512 columns
384 rows

## Slide 94
frequencies: (u,v) = (4,3); wavelengths: (u, v) = (128,128)
wf
wf
lwf
Frequencies and Wavelengths in the Fourier Plane
512 columns
384 rows
The ratio R/C = ¾ in this image. Therefore at frequency (4,3) the wave front angle is
and the wavelength is

## Slide 95: Power Spectrum of an Image

## Slide 96: Relationship between Image and FT
power spectrum
phase
power spectrum
phase

## Slide 97: Features in the FT and in the Image
Lines in the Power Spectrum are …
… perpen-dicular to lines in the image.

## Slide 98: Fourier Magnitude and Phase
I

## Slide 99: Fourier Magnitude

## Slide 100: Fourier Phase

## Slide 101: Q: Which contains more visually relevant information; magnitude or phase?
original image
log Fourier magnitude
Fourier phase

## Slide 102: Magnitude Only Reconstruction
Phase of FT set to 0 before inverse.
Abstract expressionism?

## Slide 103: Phase Only Reconstruction
M’tude of FT set to 1 before inverse.

## Slide 104
Proof of claim made on slide 25:
Let  = -t then
where
Expand sin(·) as a Maclaurin series:
and substitute it back into the first equation,

## Slide 105
Proof of claim made on slide 25 (cont’d.):
p. 25