## Slide 1
Lecture Notes: Sharpening and Edge Enhancement

## Slide 2: Sharpening
Results from high frequency enhancement since small features correspond to short wavelength sinusoids.
Relative amplification of high frequencies in the Fourier domain corresponds to differentiation in the spatial domain.
On a discrete image, differentiation corresponds to pixel differencing.

## Slide 3: The Derivative Property of the Fourier Transform
The FT of the partial derivative w.r.t. r (in the row direction) of an image, I …
… is equal to the product of the FT of the image and the corresponding frequency variable, v.
Integration by parts
This results in horizontal HF enhancement

## Slide 4: Differentiation is Highpass Filtering
Directional derivative in r.
Vertical HF Enhancement
Directional derivative in c.
Horizontal HF Enhancement

## Slide 5: Fourier Transforms of Sums of Derivatives
Sum of first-order partial derivatives…
…linear amplification of high frequencies
Sum of second-order partial derivatives…
…quadratic amplification of high frequencies

## Slide 6: Sharpening via Differencing or Highpass Filtering
Sharpening results from adding to the image a copy of itself that has been:
Pixel-differenced in the spatial domain:
  Each pixel in the output is a difference between itself and a weighted average of its neighbors.
  Is a convolution whose weight matrix sums to 0.
Highpass filtered in the frequency domain:
  High frequencies are enhanced or amplified.
  Individual frequency components are multiplied by an increasing function of  such as  = (u2+v2), where  is a constant.

## Slide 7
Image
Right (fwd)
Difference
Sum of
Differences
Left (back)
Difference
Horizontal Differences
255
0
-255

## Slide 8: Horizontal Differencing / Sharpening
original: I(r,c)
upward diff: I(r,c)-I(r-1,c)
sharpened: 2I(r,c)-I(r-1,c)

## Slide 9: Horizontal Differencing / Sharpening
downward diff: I(r,c)-I(r+1,c)
sharpened: 2I(r,c)-I(r+1,c)
original: I(r,c)

## Slide 10: Horizontal Differencing / Sharpening
2I(r,c)-I(r-1,c)-I(r+1,c)
3I(r,c)-I(r-1,c)-I(r+1,c)
original: I(r,c)

## Slide 11: Vertical Differencing / Sharpening
backward diff: I(r,c)-I(r,c-1)
sharpened: 2I(r,c)-I(r,c-1)
original: I(r,c)

## Slide 12: Vertical Differencing / Sharpening
forward diff: I(r,c)-I(r,c+1)
sharpened: 2I(r,c)-I(r,c+1)
original: I(r,c)

## Slide 13: Vertical Sharpening
2I(r,c)-I(r,c-1)-I(r,c+1)
3I(r,c)-I(r,c-1)-I(r,c+1)
original: I(r,c)

## Slide 14: Horizontal + Vertical Sharpening
4I(r,c)-I(r,c+1)-I(r,c-1)-I(r+1,c)-I(r-1,c)
original: I(r,c)
5I(r,c)-I(r,c+1)-I(r,c-1)-I(r+1,c)-I(r-1,c)

## Slide 15: Perceptual Note
5I(r,c)-I(r,c+1)-I(r,c-1)-I(r+1,c)-I(r-1,c)
a two-level image: I(r,c) {64,192}
That our visual system does something like the edge enhancement of the disk on the left is strongly suggested by the appearance of the disk on the right. It contains only 2 intensity levels. But, we see 4 – the background, the disk, and concentric dark and bright circles surrounding the disk.

## Slide 16: Differencing / Highpass Filtering
original image, I
power spectrum

## Slide 17: Differencing / Highpass Filtering
power spectrum of h = [-1 1 0]
power spectrum of Ih = I(r,c)-I(r,c+1)

## Slide 18: Differencing / Highpass Filtering
negative pixels in differenced image
positive pixels in differenced image

## Slide 19: Differencing / Highpass Filtering
original image, I
power spectrum

## Slide 20: Image Sharpening
sharpened image, 2I(r,c)-I(r,c+1)
power spectrum
Add the differenced image, I(r,c)-I(r,c+1), back to the original to get a HF enhanced version. It is a “sharper” version of the original.

## Slide 21: Image Sharpening
original image, I
power spectrum

## Slide 22: Image Sharpening
sharpened image, 2I(r,c)-I(r,c+1)
power spectrum
Note the apparent shift to the right of the sharpened image.

## Slide 23: Image Sharpening: Edge Enhancement
Adding a differenced image back to the original increases the high frequency content. It steepens the slopes of the edges which makes the image look “sharper.” Note also that a forward difference, I(r,c)-I(r,c+1), causes the apparent edge to shift to the right.

## Slide 24
Adding a differenced image back to the original increases the high frequency content. It steepens the slopes of the edges which makes the image look “sharper.” Note also that a backward difference, I(r,c)-I(r,c-1), causes the apparent edge to shift to the left.
Image Sharpening: Edge Enhancement

## Slide 25: Sharpening: Differencing / Highpass Filtering
original image
sharpened image, 2I(r,c)-I(r,c-1)
The shift occurs because the direction of the differencing operation pushes edges in the same direction.

## Slide 26: Sharpening: Differencing / Highpass Filtering
sharpened image, 2I(r,c)-I(r,c-1)
original image
The shift occurs because the direction of the differencing operation pushes edges in the same direction. (see pp.7-8)

## Slide 27: Apparent Shift due to HF Enhancement
original
backward diff: I(r,c)-I(r,c-1)
enhanced: 2I(r,c)-I(r,c-1)

## Slide 28
enhanced: 2I(r,c)-I(r,c-1)
backward diff: I(r,c)-I(r,c-1)
original
Apparent Shift due to HF Enhancement

## Slide 29: Differentiation Through Integration
1.
2.
3.
Assume that h(ρ,χ) = δ(ρ,χ). Then Ih = I. and ∂I/∂w = ∂(Ih)/∂w.
Differentiation property of the Fourier Transform.
Convolution property of the Fourier Transform.
∂/∂w is a directional derivative with direction vector [ ]T.

## Slide 30
4.
5.
Apply 2 and 3 to 1 to get 4 & 5.
The derivative of a convolution of I by h is the convolution of I by the derivative of h.
[ ]T is a direction in the plane. w and z are projections along that direction.
Differentiation Through Integration

## Slide 31
Symmetric Differences
2
-1
-1
4
-1
-1
-1
-1
2
-1
-1
convolution matrices
0
255
-255
510
legend

## Slide 32: A note on FBUD* differences & convolution
*forward, backward, up, down
A backward difference on I is the same as
right shifting a copy of I by one pixel and subtracting it from I.

## Slide 33: A note on FBUD* differences & convolution
*forward, backward, up, down
A backward difference is the same as…
… right shifting a copy and subtracting it.
That is, to compute I(r0,c)-I(r0,c-1) …
… convolve I with h=[0 1 -1].
hb=[0 1 -1] is a backward difference whereas hf=[-1 1 0] is a forward difference.

## Slide 34: A note on FBUD* differences & convolution
*forward, backward, up, down
backward diff: I(r,c)-I(r,c-1)
enhanced: 2I(r,c)-I(r,c-1)

## Slide 35: A note on FBUD* differences & convolution
*forward, backward, up, down
original
enhanced: 2I(r,c)-I(r,c-1)

## Slide 36: Convolution Examples: Original Images

## Slide 37: Convolution Examples: Vertical Difference
signed image; 0is middle gray

## Slide 38: Convolution Examples: Horizontal Difference
signed image; 0is middle gray

## Slide 39: Convolution Examples: H + V Diff.
signed image; 0is middle gray

## Slide 40: Convolution Examples: Diagonal Difference
signed image; 0is middle gray

## Slide 41: Convolution Examples: Diagonal Difference
signed image; 0is middle gray

## Slide 42: Convolution Examples: D + D Difference
signed image; 0is middle gray

## Slide 43: Convolution Examples: H + V + D Diff.
signed image; 0is middle gray

## Slide 44: Convolution Examples: Original Images

## Slide 45: Original Image
power spectrum of I
image I

## Slide 46: Left Difference
power spectrum of Ih = I[-1 1 0]
Ih = I[0 1 -1]

## Slide 47: Original Image + Left Difference
image I
I+(Ih) = I+(I[0 1 -1])

## Slide 48: Right Difference
power spectrum of Ih = I[1 -1]
Ih = I[-1 1 0]

## Slide 49: Original Image + Right Difference
image I
I+(Ih) = I+(I[-1 1 0])

## Slide 50: Vertical Edges (L+R Diffs)
power spectrum of Ih = I[-1 2 -1]
Ih = I[-1 2 -1]

## Slide 51: Original Image + Vertical Edges
image I
I+(Ih) = I+(I[-1 2 -1])

## Slide 52: Down Difference
power spectrum of Ih = I
Ih = I

## Slide 53: Original Image + Down Difference
image I
I+(Ih) = I+( I )

## Slide 54: Up Difference
power spectrum of Ih = I
Ih = I

## Slide 55: Original Image + Up Difference
image I
I+(Ih) = I+(I )

## Slide 56: Horizontal Edges (D+U Diffs)
power spectrum of Ih = I
Ih = I

## Slide 57: Original Image + Horizontal Edges
image I
I+(Ih) = I+(I )

## Slide 58: Horiz. + Vert. Edges (L+R+D+U Diffs)
power spectrum of Ih = I
Ih = I

## Slide 59: Original Image + Horiz. + Vert. Edges
sharpened
original

## Slide 60: Original Image + Horiz. + Vert. Edges
original
sharpened

## Slide 61: Unsharp Masking
is a film-photography darkroom technique for sharpening an image. A blurred copy of the photonegative is contrast reduced and used to mask the original image.
original
blurred
negative
lo-contrast
USM
=
+

## Slide 62: Sharpening Through Blurring: Unsharp Masking
Let I be an image.
Let G be a Gaussian convolution mask.
Then J = I * G is a blurred image and K = I – J contains all the high spatial frequencies from I.
Define:
U = (1+) K + J =  K + I,
where, typically 0 <  < 2.
U is called the unsharp masking of image I.
Often, the control, α, is given as a percent value.
Then the formula is (α/100)*K+I.

## Slide 63: Sharpening Through Blurring: Unsharp Masking
original image
log power spectrum

## Slide 64: Sharpening Through Blurring: Unsharp Masking
Gaussian blur =4
log power spectrum

## Slide 65: Sharpening Through Blurring: Unsharp Masking
original minus Gaussian blur
log power spectrum

## Slide 66: Sharpening Through Blurring: Unsharp Masking
unsharp masked image
log power spectrum

## Slide 67: Sharpening Through Blurring: Unsharp Masking
unsharp masked image
original image

## Slide 68: Sharpening above a Specific Scale.
An image is sharpened by taking a linear combination of the image and a highpass filtered version of itself. The scale of the sharpening can be controlled via the cutoff of the HPF. In the following examples the image has been sharpened via
where g is a 2D Gaussian with   {1, 2, 4, 8, 16, 32, 64, 128, 256} and  is a scale factor, usually in (0,2). After the computation, each image was histogram matched to I.

## Slide 69: Sharpening above a Specific Scale
s0 = 0
Original Image

## Slide 70: Sharpening above a Specific Scale
s0 = 1, =1

## Slide 71: Sharpening above a Specific Scale
s0 = 2, =1

## Slide 72: Sharpening above a Specific Scale
s0 = 4, =1

## Slide 73: Sharpening above a Specific Scale
s0 = 8, =1

## Slide 74: Sharpening above a Specific Scale
s0 = 16, =1

## Slide 75: Sharpening above a Specific Scale
s0 = 32, =1

## Slide 76: Sharpening above a Specific Scale
s0 = 64, =1

## Slide 77: Sharpening above a Specific Scale
s0 = 128, =1

## Slide 78: Sharpening above a Specific Scale
s0 = 256, =1

## Slide 79: Sharpening above a Specific Scale
s0 = 0
Original Image

## Slide 80: Emphasizing a Specific Pass Band.
An image can be bandpass filtered by subtracting two differently Gaussian filtered copies of it. That specific band can be emphasized in the image by adding it back to the image. In the following examples the image has been emphasized via
where 0, 1  {1, 2, 4, 8, 16, 32, 64, 128, 256} and  is a scale factor, usually in (0,2). After the computation, each image was histogram matched to I.

## Slide 81: Emphasizing a Specific Pass Band
(s1,s0 ) = (1,0), =1

## Slide 82: Emphasizing a Specific Pass Band
(s1,s0 ) = (2,1), =1

## Slide 83: Emphasizing a Specific Pass Band
(s1,s0 ) = (4,2), =1

## Slide 84: Emphasizing a Specific Pass Band
(s1,s0 ) = (8,4), =1

## Slide 85: Emphasizing a Specific Pass Band
(s1,s0 ) = (16,8), =1

## Slide 86: Emphasizing a Specific Pass Band
(s1,s0 ) = (32,16), =1

## Slide 87: Emphasizing a Specific Pass Band
(s1,s0 ) = (64,32), =1

## Slide 88: Emphasizing a Specific Pass Band
(s1,s0 ) = (128,64), =1

## Slide 89: Emphasizing a Specific Pass Band
(s1,s0 ) = (256,128), =1

## Slide 90: Emphasizing a Specific Pass Band
s0 = 0
Original Image

## Slide 91: Noise Enhancement: the Problem with Sharpening
Noise occurs in every natural imaging device
  Quantum effects in CCD arrays
  Random distribution of silver halide grains in film
  Neuronal noise in the retina
Spatially independent noise
  The noise in one sensor has no effect on that in its neighbors
   the autocorrelation of the signal is an impulse at the origin
  The chances of getting repeated patterns of any frequency are virtually nil
   the frequency spectrum of the noise is flat
  Recall: Autocorrelation = inverse Fourier transform of power spectrum; Fourier transform of an impulse at (0,0) is a constant.

## Slide 92
The spectra of most natural images fall-off toward the high frequencies.
IID noise has a flat spectrum.
Therefore, at some relatively high frequency (HF) the energy in the noise is greater than that in the uncorrupted image.
Sharpening multiplies the FT of the image by u and v (or by linear combinations of them) which, at HF, increases the noise more than the uncorrupted image.
Noise Enhancement: the Problem with Sharpening

## Slide 93: Effects of Noise on Linear Enhancement of HF
noisy image
original image

## Slide 94: Effects of Noise on Linear Enhancement of HF
HF enhanced original
HF enhanced noisy image

## Slide 95: Effects of Noise on Linear Enhancement of HF
noisy image
original image

## Slide 96: Effects of Noise on Linear Enhancement of HF
HF enhanced original
HF enhanced noisy image

## Slide 97: Effects of Noise on Linear Enhancement of HF
HF enhanced original
original image

## Slide 98: Effects of Noise on Linear Enhancement of HF
noisy image
HF enhanced noisy image