## Slide 1
Lecture Notes: Sampling and Aliasing
kjfg 98

## Slide 2: Image Resampling Can Lead to the Jaggies!
zoomed × 2
The jaggies!
Warning:
Image: T. Moses, CSX SW1500 at N. Charleston, SC, Sept. 1999

## Slide 3: Downsampling (Decimation)
>> J = I(1:2:R,1:2:C,:);
E.g.: every 2nd pixel in every 2nd row
This is a bad way to do it.

## Slide 4: Downsampling (Decimation)
>> J = I(1:2:R,1:2:C,:);
E.g.: every 2nd pixel in every 2nd row
Bad, bad – very bad.

## Slide 5: Jaggies and Moire
↓×3
↑×3
original image
decimated by 3×
upsampled by 3×
Another fine mess: Moire distortion.
Images: C. Burnett, Wikimedia Commons, http://en.wikipedia.org/wiki/File:Moire_pattern_of_bricks.jpg

## Slide 6: Power Spectrum from Discrete Fourier Transform
Recall:
DFT

## Slide 7: Power Spectrum from Discrete Fourier Transform
The DFT of an image is the same size as the image.
DFT
decimated image
power spectrum
Recall:

## Slide 8: The Scaling Property of the FT
This implies that if an image is reduced in size, its features in the spatial domain become smaller and its features in the frequency domain become larger.
Recall:

## Slide 9: The Uncertainty Relation
FT
space
frequency
FT
space
frequency
A small object in space has a large frequency extent and vice-versa.
If ΔxΔy is the extent of the object in space and if ΔxΔy is its extent in frequency then
Recall:

## Slide 10: Effect of Decimation on the DFT of an Image
Decimation of an R×C image, I, by a factor of n results in an R/n × C/n image, J.
The DFT of image J is the same size as J.
The uncertainty relation implies that the FT of J should be (R-1) × (C-1) < n R/n × n C/n ≤ R × C.
Contradiction?
Q: How can these 3 facts be true simultaneously?
A: The FT of J folds over or aliases itself on the DFT of J because the DFT is defined on a torus.

## Slide 11: Discrete FT is on a Torus
Recall: the DFT of a digital image assumes the image has a toroidal topology…

## Slide 12: Discrete Fourier Transform is on a Torus
… which implies that the result also has a toroidal topology.

## Slide 13: Discrete FT is on a Torus
Point 1 (p. 9)
If the image is made smaller the torus is likewise …

## Slide 14: Discrete FT is on a Torus
… and the DFT is the same size.
Point 2 (p. 9)

## Slide 15: Ideal PS of 2× Decimated Image
zoomed × 2
One might assume that the smaller DFT is the central region of the larger … but it’s not.

## Slide 16: To Make Actual PS of 2 × Decimated Image:
All of the larger one is present in the smaller one.
low freqs.
high freqs. of cols.
low freqs. of rows
of cols & rows
low freqs. of cols.
high freqs. of rows
high freqs.
of cols & rows
Partition F{I} into these four parts, …

## Slide 17: Actual PS of 2× Dec:
… four parts that are contiguous on the full-sized DFT torus.

## Slide 18: Actual PS of 2× Decimated Image
Each of the 4 PS regions forms a torus. The 4 torii are superpositioned onto 1.
low freqs.
high freqs. of cols.
low freqs. of rows
of cols & rows
high freqs.
of cols & rows
low freqs. of cols.
high freqs. of rows

## Slide 19: DFT Aliasing on the Torus
The 4 superpositioned torii alias the high frequencies onto the low frequencies.

## Slide 20: PS of Original and PS of 2× Decimated Image
original
decimated × 2, zoomed × 2
Aliased frequency-plane features …

## Slide 21: Original Image and 2× Decimated Image
decimated × 2, zoomed × 2
original
… lead to jaggies in the decimated image.

## Slide 22: First Alternative Explanation of Aliasing
The aliasing phenomenon can be described in terms of the so-called “wagon wheel” effect. The name comes from the appearance in a 24 frame per second movie of a wagon wheel rotating slightly faster than 12 frames per second. It appears to be rotating slowly backward.

## Slide 23: Signal Aliasing
An under-sampled sinusoid is a sinusoid of a different frequency.
Figure from George Bebis, Univ. of Nevada, Reno, CS474, Image Processing and Interpretation, Lecture 4.3.

## Slide 24: Nyquist-Shannon & Whittaker-Shannon Sampling
If a function [signal or image] x(t) contains no frequencies higher than B hertz, it is completely determined by giving its ordinates at a series of points spaced 1/(2B) seconds apart. In other words, a band-limited function can be perfectly reconstructed from a countable sequence of samples if the band limit, B, is no greater than half the sampling rate (samples per second).1
Given a sequence of real numbers, x[n], the continuous function:
1http://en.wikipedia.org/wiki/Nyquist–Shannon_sampling_theorem
has a Fourier transform, X( f ), whose non-zero values are confined to the region: | f | ≤ 1/2T. When parameter T has units of seconds, the band limit, 1/2T, has units of cycles/sec (hertz). When the x[n] sequence represents time samples, at interval T, of a continuous function, the quantity fs = 1/T is known as the sample rate, and fs/2 is the corresponding Nyquist frequency. When the sampled function has a bandlimit, B, less than the Nyquist frequency, x(t) is a perfect reconstruction of the original function.2
2http://en.wikipedia.org/wiki/Whittaker–Shannon_interpolation_formula

## Slide 25: Second Alternative Explanation of Aliasing
The aliasing phenomenon can also be described in terms of the convolution property of the Fourier Transform. In fact, this is the way it is usually explained.

## Slide 26: The Sampling Function
The sampling function is a set of impulses evenly spaced on a grid.
27

## Slide 27: The Sampling of an Image
An image is sampled by multiplying it by the sampling function

## Slide 28: Image Sampling in the Spatial Domain
This results in an image whose pixels have the values of the original image at the impulse locations.

## Slide 29: Convolution Property of the Fourier Transform
The Fourier Transform of a product equals the convolution of the Fourier Transforms. Similarly, the Fourier Transform of a convolution is the product of the Fourier Transforms

## Slide 30: The Fourier Transform of the Sampling Function
The Fourier Transform of the sampling function is another sampling function but with impulses 1/N apart.
Cf. slide 23

## Slide 31: Convolution by an Impulse
An impulse is a digital image, that has a single pixel with value 1; all others have value zero. An impulse at location (r, c) is represented by:
If an image is convolved with an impulse at location (r, c), the image is shifted in location down by r pixels and to the right by c pixels.

## Slide 32: Convolution by an Impulse
The convolution of any function with a delta function translates the function to the location of the impulse.

## Slide 33: The Fourier Transform of a Sampled Image
If the support of
has a radius  1/(2N) then there will be overlap — aliasing
The sampling of image I causes its Fourier Transform
to be repeated at intervals of 1/N.

## Slide 34: The FT of a Sampled Image with No Aliasing
For aliasing not to occur the frequency support of I must have a radius of < 1/(2N)

## Slide 35: Part of the Transform Computed by the FFT
Although the FT of the sampled image continues on indefinitely in theory, only one copy of the complete pattern is required for processing. The Fast Fourier Transform (FFT) algorithm computes the transform with the origin in the upper left. Usually the transform is displayed with the origin in the center.
as computed
(aliasing)
origin shifted
(aliasing)
as computed
(no aliasing)
origin shifted
(no aliasing)

## Slide 36: Filtering Before Downsampling to Prevent Aliasing
That is equivalent to convolving I(r,c)
with a spatial filter of width 2N.
Thus, to down-sample I(r,c) by a factor of 2, use a spatial filter of width 4. Since this is midway be-tween 3 and 5, use a 5x5 convolution mask.
FT
If the image is a bit blurry then a 3x3 will usually suffice
that
To sample I(r,c) every N pixels multiply I(u,v) = F{I} by a window H(u,v) such

## Slide 37
Filtering to Prevent Aliasing
original image
power spectrum

## Slide 38
Filtering to Prevent Aliasing
to decimate original by 2 …
… zero outside red square.

## Slide 39
Filtering to Prevent Aliasing
Notice the shift & ringing in the result
ideal filter
zoomed × 2

## Slide 40
Filtering to Prevent Aliasing
To reduce ringing try multiplying the FT
by a Gaussian w/ (v,u)=(¼R, ¼C)

## Slide 41
Filtering to Prevent Aliasing
PS of FT × Gaussian
ringing is reduced but result is blurry
zoomed × 2

## Slide 42
Filtering to Prevent Aliasing
try multiplying the FT
by a Gaussian w/ (v,u)=(½R, ½C)

## Slide 43
Filtering to Prevent Aliasing
PS of FT × Gaussian
some aliasing but result is less blurry
zoomed × 2

## Slide 44
Filtering to Prevent Aliasing
zoomed × 2
ideal filtered
original

## Slide 45
Filtering to Prevent Aliasing
original
Gaussian w/ (v,u)=(¼R, ¼C)
zoomed × 2

## Slide 46
zoomed × 2
Filtering to Prevent Aliasing
Gaussian w/ (v,u)=(½R, ½C)
original

## Slide 47
zoomed × 2
Filtering to Prevent Aliasing
original
decimated by factor of 2
zoomed × 2

## Slide 48: Reconstruction of a Downsampled Image
A band-limited image that was downsampled by a factor of two can be reconstructed – upsampled – using the Fourier Transform.
Simply copy the FT of the downsampled image into the center of a complex-valued image of all zeros that has twice the dimensions of the downsampled image. Then take the inverse FT.
This follows from the FT that results from multiplying the image with a “checkerboard” sampling grid. The following example with a Gaussian distribution demonstrates this.

## Slide 49: Reconstruction
512768 image with a centered, =4 Gaussian.

## Slide 50: Reconstruction
256384 image of downsampled (1:2:512,1:2:768) =4 Gaussian.

## Slide 51: Reconstruction
Power spectrum of centered, =4 Gaussian.

## Slide 52: Reconstruction
Power spectrum of downsampled =4 Gaussian.

## Slide 53: Reconstruction
512768 image with a 2 sampling grid

## Slide 54: Reconstruction
=4 Gaussian multiplied by sampling grid.

## Slide 55: Reconstruction
PS of sample-grid multiplied, =4 Gaussian.

## Slide 56: Reconstruction
Compare that to the FT of the original.

## Slide 57: Reconstruction
PS from cropped FT of sample-grid multiplied =4 Gaussian.

## Slide 58: Reconstruction
IFT of cropped sample-grid mpy’d FT of =4 Gaussian.

## Slide 59: Reconstruction
zero-padded cropped FT of sample-grid multiplied =4 Gaussian.

## Slide 60: Reconstruction
=4 Gaussian reconstructed from zero-padded FT.

## Slide 61: Reconstruction
Original 512768 image with a centered, =4 Gaussian.