## Slide 1
Lecture Notes: Reduction of Uncorrelated Noise

## Slide 2: Noise in Images
All images created through optical projection onto a sensor array are noisy.
Uncorrelated noise
  Quantum noise in CCD arrays
  Silver halide grains in film photography
  Neuronal noise in a retina
  Quantization noise in digital photographs
Correlated noise
  Due to electrical interference
  Due to source / sensor interference
  Halftone distortion / moiré patterns

## Slide 3: Image with Additive Noise
undegraded image
noisy image
additive noise
spatial domain
undegraded image
noisy image
additive noise
frequency domain

## Slide 4: Uncorrelated Noise
Intensity distributions – normalized histograms
Each pixel’s value has probability of occurrence given by the associated distribution.

## Slide 5: Uncorrelated Noise
Each pixel’s value has probability of occurrence given by the associated distribution.
… black pixels occur 75% of the time and
white pixels occur 25% of the time.
All values occur with equal probability.
This is sparse noise: Only 12.5% of the pixels contain noise. Of those 12.5% …
The most likely value is 128 with an average difference of 25 from 128 (std. dev.).
Intensity distributions – normalized histograms

## Slide 6: Uncorrelated Color Noise: Gaussian

## Slide 7: Uncorrelated Color Noise: Uniform

## Slide 8: Noise Enhancement: Problem with Sharpening
Noise occurs in every natural imaging device
  Quantum effects in CCD arrays
  Random distribution of silver halide grains in film
  Neuronal noise in the retina
Spatially independent noise
  The noise in one sensor has no effect on that in its neighbors
   the autocorrelation of the signal is an impulse at the origin
  The chances of getting repeated patterns of any frequency are virtually nil
   the frequency spectrum of the noise is flat
  Recall: Autocorrelation = inverse Fourier transform of power spectrum; Fourier transform of an impulse at (0,0) is a constant.

## Slide 9: Noise Enhancement: Problem with Sharpening
The spectra of most natural images fall-off toward the high frequencies.
IID noise has a flat spectrum.
Therefore, at some relatively high frequency (HF) the energy in the noise is greater than that in the uncorrupted image.
Sharpening multiplies the FT of the image by u and v (or by linear combinations of them) which, at HF, increases the noise more than the uncorrupted image.

## Slide 10: Gaussian IID Noise Field
 = 128
s = 32
IID: Independent, Identically Distributed
IID  no spatial correlation

## Slide 11: Gaussian IID Noise Field
IID  no spatial correlation
… is this number divided by the number of pixels in the image.
 = 128
s = 32
IID: Independent, Identically Distributed
2
The probability of any one pixel having this value …
1

## Slide 12: Autocorrelation of an Image
Let the support of I be a torus. (I is defined on a torus a la the Fourier transform.)
Let be I minus the mean value of I. Make a copy of . Shift the copy by (r,c) on the torus. Pixel-wise multiply the shifted version by the original and sum the products.
AI(ρ,χ), the autocorrelation of I at offset (ρ,χ), is a measure of the similarity of I to itself when shifted by (ρ,χ).

## Slide 13: Power Spectrum & Autocorrelation of IID Noise
Power Spectrum
Autocorrelation
0
C/2
-C/2
 = 0
c
The autocorrelation is the inverse FT of the power spectrum.

## Slide 14: Power Spectrum & Autocorrelation of IID Noise
Power Spectrum
Autocorrelation
0
C/2
-C/2
 = 0
c
The autocorrelation of an IID noise image is ≈ δ(ρ,χ). That implies the PS is ≈ constant

## Slide 15: Noise-Free Image and Uncorrelated Noise Field
Gaussian noise field
image

## Slide 16
noise field center row log power spectrum
image center row log power spectrum
IID noise spectrum is flat.
Image spectrum falls off.
Spectra of Noise-Free Image and Uncorr. Noise Field

## Slide 17
image + noise field
image + noise field center row log PS
Noise energy exceeds image energy beyond a certain freq.
Sum of Noise-Free Image and Uncorrelated Noise Field

## Slide 18: Power Spectra of Noise-Free Image and Noise Field
noise image
original image

## Slide 19: Power Spectra of Sum of Image and Noise Field
original image
noisy image

## Slide 20: Power Spectra of Sum of Image and Noise Field
blue indicates noise > image
original image

## Slide 21: Power Spectra of Sum of Image and Noise Field
red indicates image > noise
noise image

## Slide 22: Power Spectra of Sum of Image and Noise Field
image & noise
noisy image

## Slide 23: Additive Noise: Another Example
original image
noise image
image+noise

## Slide 24: Additive Noise: Another Example
image PS
noise PS
image+noise PS
displayed:

## Slide 25: Additive Noise: Another Example
image PS
image PS > noise PS
image+noise PS
displayed:

## Slide 26: Additive Noise: Reduce Through Blurring?
red indicates image > noise
image PS > noise PS
f0
f0
At some frequency, f0, there are more components where the noise power is greater than the image power.

## Slide 27: Additive Noise: Reduce Through Blurring?
pass
reject
pass
reject
red indicates image > noise
image PS > noise PS
Thus, it makes sense to apply a LPF with cutoff f0, (a blurring filter) to the images and see what happens.

## Slide 28: Additive Noise: Reduction Through Blurring.
PS of Gaussian blurred image
Gaussian Blurred Image
The result is actually no better. There’s less noise but the blurring looks worse.

## Slide 29: Additive Noise: Reduction Through Blurring.
PS of Gaussian blurred image
Gaussian Blurred Image
The result is actually no better. There’s less noise but the blurring looks worse.

## Slide 30: Noise Masking
red: image > noise
blue: image < noise
power spec. of noisy image
If the freq. comps. for which noise-power > image-power are known1…
1of course they almost never are.

## Slide 31: Noise Masking
… mask those out of the FT and invert the result to get…
image < noise masked out
power spec. of noisy image

## Slide 32: Noise Masking
noisy image
noise-masked mage
… this:

## Slide 33: Noise Masking
blurred noisy image
noise-masked mage
Although the noise-masked image looks better than the blurred one, it is still noisy. Moreover, this example is unrealistic because we know the exact noise power spectrum. In any real case we will at most know its statistics.

## Slide 34: Image Degradation Model
undegraded image
additive noise
degraded image
pointspread function
So far, we have considered only additive noise. Before going further it will be useful to consider a more general model of image degradation, one that includes convolution with a pointspread1 function, H, as well as additive noise.
1H is also referred to as the optical transfer function.

## Slide 35: Pointspread Operators
A pointspread operator is a linear model of the distortion acquired during the imaging process. Since it is a linear model, it is a convolution operator. One example of this is aperture distortion, an unavoidable consequence of making an image with a camera that has an opening larger than a point.

## Slide 36: Pointspread Operators
pinhole camera
aperture camera
A pinhole camera maps one object point to one image point; it is one-to-one.
An aperture camera maps one object point to many image points; it spreads the points.

## Slide 37: Pointspread Operators and Convolution
Recall how a convolution works through multiply, shift, and add (See Lect. 7 p. 25ff). That is precisely the effect of imaging through an aperture. It results in a blurry image.

## Slide 38: Lenses
A properly designed lens will focus the light emanating from a point and thereby reduce the blurring. But no lens can do this perfectly. In fact, the lens adds its own distortion. The result is an optical transfer function, H(r,c), that is convolved with the image.

## Slide 39: Image Degradation Model
undegraded image
additive noise
degraded image
pointspread function
Note: The term pointspread operator refers to convolution by the pointspread function.

## Slide 40: Image Degradation Model

## Slide 41: Image Degradation Model (Frequency Domain)
undegraded image
additive noise
degraded image
pointspread operator

## Slide 42: Image Degradation Model (Frequency Domain)
Images shown are log magnitude.

## Slide 43: Image Restoration
Let I be a perfect image and let K be the image convolved with a pointspread function, H. Then in the frequency domain:
If the process of imaging adds noise then we get J = K + N, or in freq.:
We want a filter, W, to remove as much of the noise from J as possible:
Then an estimate of I would be the inverse Fourier transform of
We want to find the filter, W, that results in the closest possible estimate of I i.e. the W that minimizes the energy of the difference between the estimate and I.
That is we want to find W such that
is as small as possible. This is called least mean squared (LMS) minimization.

## Slide 44: Image Restoration
There are a number of ways to solve for the minimum squared error. All make use of the assumption that the image and the noise are uncorrelated. Depending on how that fact is used, slightly different solutions are found. The most common one used in image processing is the Wiener filter:
For frequencies (u,v) where noise power is smaller than the image power W acts like an inverse filter since N(u,v)/I(u,v) < 1 and
Then, with a little bit of algebra, we get
and at frequencies where the noise power dominates, N(u,v)/I(u,v) > 1 and
the fraction is small so the noise power is diminished.

## Slide 45: Image Restoration
This is one of the possible derivations of the Wiener filter

## Slide 46: Image Restoration
From the previous page, the squared error is
The second term should be small compared to the first since it can be written
and the image and the noise are assumed to be uncorrelated1. Thus the error can be approximated by
The mean squared error, ε2, is minimized when W is given by,

## Slide 47: Noise Reduction Through LMS Filtering1
Gaussian noise field
image
1Here the PSF is the identity.

## Slide 48: Noise Reduction Through LMS Filtering1
noisy image
image
1Here the PSF is the identity.

## Slide 49: Additive Noise (Power Spectra)
noisy image
original image

## Slide 50: Additive Noise (Power Spectra)
Wiener filter
noisy image
In this example we knew the exact image and noise power spectra and the PSF was the identity because the image is synthetic. In a real example, none of that is true.

## Slide 51: Additive Noise (Power Spectra)
Wiener filter
noisy image

## Slide 52: Additive Noise (Power Spectra)
original image
Wiener filtered image

## Slide 53: Additive Noise
Wiener filtered image
noisy image

## Slide 54: Additive Noise
Wiener filtered image
original image

## Slide 55: Additive Noise
Gaussian blurred image
original image

## Slide 56: Noise Reduction Through LMS Filtering1
noisy image J = I*h + N
image
1Least Mean Squared. PSF, h, is Gaussian m=0, s=2.

## Slide 57: Image*PSF + Noise (Power Spectra)
original image
noisy image J = I*h + N

## Slide 58: Image*PSF + Noise (Power Spectra)
Wiener filter
Wiener filtered image
In this example we knew the exact image and noise power spectra and the PSF was Gaussian w/ μ=0, σ=2. In a real example, none of that is true.

## Slide 59: Image*PSF + Noise (Power Spectra)
Wiener filter
Wiener filtered image

## Slide 60: Image*PSF + Noise (Power Spectra)
original image
Wiener filtered image

## Slide 61: Image*PSF + Noise
Wiener filtered image
noisy image J = I*h + N

## Slide 62: Image*PSF + Noise
Wiener filtered image
original image

## Slide 63: LMS Image Restoration (Real Example)
For this real example we need to estimate the image power spectrum, the pointspread function and the noise power spectrum.

## Slide 64: LMS Image Restoration (Real Example)
To estimate the noise power spectrum, analyze a constant area from the image.

## Slide 65: Noise Estimation
+
-
+
original
blurred w/ Gaussian σ=5
difference
σR = 5.0981 σG = 4.0672
σB = 6.9212
Find the std. deviations of each band:

## Slide 66: Pointspread Function Estimation
To estimate the PSF, find the image of a point and construct a convo-lution mask from it.

## Slide 67: Wiener Filter Estimation

## Slide 68: LMS Image Restoration (original)

## Slide 69: LMS Image Restoration (filtered)

## Slide 70: Detail of Results
filtered image
original image
matlab’s wiener2
The contrast of these has been increased to make the differences more visible.