## Slide 1
Lecture Notes on Mathematical Morphology: The Median Filter

## Slide 2: The Median Filter
Returns the median value of the pixels in a neighborhood
Is non-linear
Is a morphological filter
Is similar to a uniform blurring filter which returns the mean value of the pixels in a neighborhood of a pixel
Unlike a mean value filter the median tends to preserve step edges
original
median filtered

## Slide 3: Median Filter: General Definition
This can be computed as follows:
Let I be a monochrome (1-band) image.
Let Z define a neighborhood of arbitrary shape.
At each pixel location, p = (r,c), in I …
… select the n pixels in the Z-neighborhood of p,
… sort the n pixels in the neighborhood of p, by
The output value at p is L(m), where m = n/2+1.
value, into a list L( j) for j = 1,…,n.

## Slide 4: Median Filter: General Definition
sorted intensity values from neighborhood of p.
131
133
133
136
140
143
147
152
154
157
160
162
163
164
165
171
p
median assigned to pixel loc p in output image.

## Slide 5: A Noisy Step Edge

## Slide 6: Blurred Noisy 1D Step Edge

## Slide 7: Blurred Noisy 1D Step Edge
J(32-4:32+4)=
0.1920
0.3416
0.0464
0.0177
0.3062
1.3043
1.0079
1.0082
1.0950
J(33-4:33+4)=
0.3416
0.0464
0.0177
0.3062
1.3043
1.0079
1.0082
1.0950
1.2935
0.5910
0.7134
mean
mean

## Slide 8: Median Filtered Noisy 1D Step Edge

## Slide 9: Median Filtered Noisy 1D Step Edge
J(32-4:32+4)=
0.1920
0.3416
0.0464
0.0177
0.3062
1.3043
1.0079
1.0082
1.0950
0.0177
0.0464
0.1920
0.3062
0.3416
1.0079
1.0082
1.0950
1.3043
J(33-4:33+4)=
0.3416
0.0464
0.0177
0.3062
1.3043
1.0079
1.0082
1.0950
1.2935
0.0177
0.0464
0.3062
0.3416
1.0079
1.0082
1.0950
1.2935
1.3043
sorted
sorted
median
median

## Slide 10: Median vs. Blurred
step
noisy
blurred
median
The median filter preserves the step edge better than the blurring filter.

## Slide 11: Median vs. Blurred
median
blurred
step
The median filter preserves the step edge better than the blurring filter.

## Slide 12: Median vs. Blurred
blurred
median
step
The median filter preserves the step edge better than the blurring filter.

## Slide 13: Median Filtering of Binary Images
Original
Noisy

## Slide 14: Median Filtering of Binary Images
Median Filtered Noisy
Original

## Slide 15: Filtering of Grayscale Images
Original
Noisy

## Slide 16: Filtering of Grayscale Images
Noisy
Noisy

## Slide 17: Filtering of Grayscale Images
3x3-median x 1
3x3-blur x 1

## Slide 18: Filtering of Grayscale Images
3x3-median x 2
3x3-blur x 2

## Slide 19: Filtering of Grayscale Images
3x3-median x 3
3x3-blur x 3

## Slide 20: Filtering of Grayscale Images
3x3-median x 4
3x3-blur x 4

## Slide 21: Filtering of Grayscale Images
3x3-median x 5
3x3-blur x 5

## Slide 22: Filtering of Grayscale Images
3x3-median x 10
3x3-blur x 10

## Slide 23: Filtering of Grayscale Images
Noisy
Noisy

## Slide 24: Limit and Root Images
Fact: if you repeatedly filter an image with the same blurring filter or median filter, eventually the output does not change. That is, let
Then
where n and m are integers (< ∞) , I0 is a single-valued image and Ir is called the median root of I.

## Slide 25: Limit and Root Images
3x3-median x 10
3x3-blur x 10

## Slide 26: Limit and Root Images
3x3-median root
3x3-blur x n

## Slide 27: Median Filter Algorithm in Matlab
function D = median_filt(I,SE,origy,origx)
[R,C] = size(I); % assumes 1-band image
[SER,SEC] = size(SE); % SE < 0  not in nbhd
N = sum(sum(SE>=0)); % no. of pixels in nbhd
A = -ones(R+SER-1,C+SEC-1,N); % accumulator
n=1; % copy I into band n of A for nbhd pix n
for j = 1 : SER % neighborhood is def’d in SE
for i = 1 : SEC
if SE(j,i) >= 0 % then is a nbhd pixel
A(j:(R+j-1),i:(C+i-1),n) = I;
n=n+1; % next accumulator band
end
end
end
% pixel-wise median across the bands of A
A = shiftdim(median(shiftdim(A,2)),1);
D = A( origy:(R+origy-1) , origx:(C+origx-1) );
return;

## Slide 28: Vector Median Filter
A vector median filter selects from among a set of vectors, the one vector that is closest to all the others.
That is, if S is a set of vectors, in Fn the median, v, is
Fn is an n-dimensional linear vector space over the field, F.)

## Slide 29: Vector Median Filter
A vector median filter selects from among a set of vectors, the one vector that is closest to all the others.
That is, if S is a set of vectors, in Fn the median, v, is
Fn is an n-dimensional linear vector space over the field, F.)

## Slide 30: Color Median Filter
If we let Fn = R3 then the vector median can be used as a color median filter.
(a)
(b)
(c)
(d)
(a) original image
(b) image (a) with sparse noise
(c) image (b) color median filtered
(d) image (c) color median filtered
Median filter performed on 3×3 nbhd.
original image: Jim Woodring
www.jimwoodring.com

## Slide 31: Color Median Filter
noisy
3×3 MF
(3×3 MF)2
original
3×3 MF
(3×3 MF)2
The output color at (r,c) is always selected from a nbhd of (r,c) in the input image.

## Slide 32: Color Median Filter
noisy
3×3 MF
(3×3 MF)2
original
3×3 MF
(3×3 MF)2
The output color at (r,c) is always selected from a nbhd of (r,c) in the input image.

## Slide 33: Color Median Filter
noisy
3×3 MF
(3×3 MF)2
original
3×3 MF
(3×3 MF)2
The output color at (r,c) is always selected from a nbhd of (r,c) in the input image.

## Slide 34: Color Median Filter
noisy
3×3 MF
(3×3 MF)2
original
3×3 MF
(3×3 MF)2
The output color at (r,c) is always selected from a nbhd of (r,c) in the input image.

## Slide 35: Color Median Filter
Jim Woodring – A Warm Shoulder
www.jimwoodring.com
Sparse noise, 32% coverage in each band

## Slide 36: Color Median Filter
3×3 color median filter applied twice
3×3 color median filter applied once
original image: Jim Woodring
www.jimwoodring.com

## Slide 37: Color Median Filter
Jim Woodring – A Warm Shoulder
www.jimwoodring.com
Sparse noise, 32% coverage in each band

## Slide 38: Color Median Filter
(3×3 CMF2 of noisy) – original
(3×3 CMF2 of noisy) – (3×3 CMF2 of original)
Absolute differences displayed as negatives to enhance visibility
original image: Jim Woodring
www.jimwoodring.com

## Slide 39: CMF vs. Standard Median on Individual Bands
A color median filter has to compute the distances between all the color vectors in the neighborhood of each pixel. That’s expensive computationally.
Q: Why not simply take the 1-band median of each color band individually?
A: The result at a pixel could be a color that did not exist in the pixel’s neighborhood in the input image. The result is not the median of the colors – it is the median of the intensities of each color band treated independently.
Q: Is that a problem?
A: Maybe. Maybe not. It depends on the application. It may make little difference visually. If the colors need to be preserved, it could be problematic.

## Slide 40: CMF vs. Standard Median on Individual Bands
Jim Woodring – A Warm Shoulder
www.jimwoodring.com
Sparse noise, 32% coverage in each band

## Slide 41: CMF vs. Standard Median on Individual Bands
3×3 color median filter applied twice
3×3 color median filter applied once
original image: Jim Woodring
www.jimwoodring.com

## Slide 42: CMF vs. Standard Median on Individual Bands
original image: Jim Woodring
www.jimwoodring.com
3×3 median filter applied to each band twice
3×3 median filter applied to each band once

## Slide 43: CMF vs. Standard Median on Individual Bands
Jim Woodring – A Warm Shoulder
www.jimwoodring.com
Sparse noise, 32% coverage in each band

## Slide 44: CMF vs. Standard Median on Individual Bands
Fraction of pixels in CMF2 noisy image identical to original: 0.29
Fraction of pixels in CMF2 noisy image identical to CMF2 original: 0.43
Fraction of pixels in MF2 noisy image identical to original: 0.14
Fraction of pixels in MF2 noisy image identical to MF2 original: 0.28
original image: Jim Woodring
www.jimwoodring.com